## Slide 1: Introduction to Side-Channel Analysis
Jiun-Peng CHEN Oct. 13, 2023
Department of Electrical Engineering

## Slide 2: Side-Channel Analysis (Attack)
extra source of information
Notes: 那以這張圖來說，旁通道分析就像是車輛不經過這閘門，從旁邊繞到過去。 其實我這邊顏色有對應，紅色就像是要分系破解，可以需要暴力破解或有金鑰。可想像車輛藉由綠色的草坪，繞過紅色閘門答到目的。 以這張圖來說，就是繞過去不用付錢。

## Slide 3: Side-Channel Analysis (Attack)
In cryptography, a Side-Channel Analysis is any attack based on information gained from the physical implementation of a cryptosystem rather than brute force or theoretical weaknesses in the algorithms (compare cryptanalysis).
For example, timing information, power consumption, electromagnetic leaks, or even sound can provide an additional source of information, which can be exploited to break the system.
Paul Kocher 1973-
https://en.wikipedia.org/wiki/Side-channel_attack
https://en.wikipedia.org/wiki/Paul_Carl_Kocher

## Slide 5
2022 The ACM Conference on Computer and Communications Security (CCS)
IACR Transactions on Cryptographic Hardware and Embedded Systems (TCHES)

## Slide 6: Power Analysis Attacks (Ch. 1-3, 6)
https://link.springer.com/book/10.1007/978-0-387-38162-6
http://dpabook.iaik.tugraz.at/
Graz University of Technology, Austria
University of Bristol, UK
Thomas Popp
Elisabeth Oswald,
Stefan Mangard,

## Slide 7: Outline
Introduction
Cryptographic Devices
Power Consumption
Research Papers
Advanced Encryption Standard
Power Analysis and Countermeasure
Conclusion

## Slide 8: 1. Introduction
Cryptographic Algorithms
Attacks on Cryptographic Devices
Power Analysis Attacks
Countermeasures Against Power Analysis Attack

## Slide 9: Cryptographic Algorithms
Auguste Kerckoffs’s Principle

## Slide 10: Modern Cryptography (1976-)
Symmetric-key cryptography
  Uses the same cryptographic keys for both plaintext encryptions and ciphertext decryption.
  DES, AES (Advanced Encryption Standard)
  Differential Power Analysis, DPA (1999) 2023/10/12 Times Cited: 10508
  Lightweight Cryptography (2023: ASCON)
Public-key cryptography
  Uses key pairs: public keys and private keys.
  RSA, ECC (Elliptic Curve Cryptography)
  Simple Power Analysis, SPA (1996) 2023/10/12 Times Cited: 6716
  Post-Quantum Cryptography (2022: Kyber, Dilithium, and SPHINCS+)

## Slide 11: Attacks on Cryptographic Devices
Invasive
Semi-invasive
Non-invasive
Active
(Fault Injection)
Passive
Cache Attack
Tamper the context or not
The Degree of de-packaging

## Slide 12: Invasive and Semi-invasive

## Slide 13: Attacks on Cryptographic Devices
Invasive
Semi-invasive
Non-invasive
Active
(Fault Injection)
Passive
Tamper the context or not
The Degree of de-packaging
Side-Channel Analysis:
Cache Attack

## Slide 14: Power Analysis Attacks
Power Consumption
  Data-Dependency
  Operation-Dependency
Simple Power Analysis
  Just a few power trace
Differential Power Analysis
  More power traces

## Slide 15: Countermeasures
Goal
  Remove the dependency of intermediate values
  Hiding
    Remove data-dependency
    Cannot be removed completely
  Masking
    Randomize intermediate values
    Can still be data-dependent
Session Keys
  Key should be updated as frequently as possible

## Slide 16: 2. Cryptographic Devices
Cryptographic Devices
  Implement algorithms and store keys
  Smart card, USB token, RFID tag, etc.
Security
  Should not rely on the secrecy of the implementation
https://shop.ledger.com/pages/ledger-nano-s-plus
https://store.google.com/us/product/titan_security_key?hl=en-US

## Slide 17: Components
Dedicated Cryptographic Hardware
General-Purpose Hardware
Cryptographic Software
Memory
Interface

## Slide 18: Design and Implementation
Digital Circuits
  ASIC (Application-Specific Integrated Circuit)
    Logic cells are customized for high-performance, small area, etc.
  FPGA (Field Programmable Gate Array)
    Use logic cells in the FPGA board

## Slide 19: Custom Design
Design Steps
  Specification
  Behavioral Design
  Structural Design
  Physical Design
    ASIC
    FPGA

## Slide 20: Logic Cells
Type:
  Combinational Cells
  Sequential Cells
Complementary CMOS Logic Style
A Logic cell consists of:
  a Pull-up Network (PUN) (composed of PMOSs)
  a Pull-down Network (PDN) (composed of NMOSs)
2-input CMOS NOR Gate
2-input CMOS NAND Gate
A. S. Sedra, K. C. Smith, T. C. Carusone, V. Gaudet, Microelectronic Circuits, 7th ed. Oxford University Press, 2020

## Slide 21: 3. Power Consumption
  Static power consumption:
  PUN/PDN does not conduct simultaneously.
  Leakage current (quite small)
Dynamic power consumption:
  Lumped-C model:
    Intrinsic & extrinsic capacitance
    Lumped together in to a single capacitance
Dynamic Power >> Static Power
  Data dependency
0
1
-> 1
Discharging current
-> 0
-> 0
Charging Current
-> 1
Short-circuit current
A. S. Sedra, K. C. Smith, T. C. Carusone, V. Gaudet, Microelectronic Circuits, 7th ed. Oxford University Press, 2020

## Slide 22: Dynamic Power Consumption
S. Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards. New York, NY, USA: Springer, 2006

## Slide 23: Models
Hamming Distance (HD) model
  Map transitions to power consumption values
  Buses and registers
Hamming Weight (HW) model
  The more bits are set to the same value the better
  Only resort to HW model if HD model cannot be applied
Other Models
  Different weights for different types of transitions
  Power consumption of larger parts of a circuit

## Slide 24: Software Power Model
Data transferred between memory and CPU
CPU
Memory
value
Bus
# bitflips = HW(value)

## Slide 25: Hardware Power Model
Combinational Logic
Register
# bitflips = HD(statei , statei+1) = HW(statei ⊕ statei+1)
state0
state1
state1
state2

## Slide 26: Noise
Power Supply, Clock Generator
Conducted and Radiated Emissions
Quantization Noise
Switching Noise
Caused by cells that are not relevant
S. Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards. New York, NY, USA: Springer, 2006

## Slide 27: Measurement Setups
S. Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards. New York, NY, USA: Springer, 2006

## Slide 28: Electromagnetic Measurement
By power measurement circuits → the simplest way is to insert a small resistor between the power supply and GND
By EM probes
IEC standard 61967
→ define how conducted emissions and radiated emissions should be measured in order to test the EMC of an IC

## Slide 30
4. Research Papers

## Slide 31: Cloning 3G/4G SIM Cards (Black Hat USA 2015) Hardware Wallets (Ledger, TREZOR… 2015-2019)
https://www.youtube.com/watch?v=qKCQ1KL9GEc
https://www.blackhat.com/docs/us-15/materials/us-15-Yu-Cloning-3G-4G-SIM-Cards-With-A-PC-And-An-Oscilloscope-Lessons-Learned-In-Physical-Security-wp.pdf
Jochen Hoenicke. Extracting the Private Key from a TREZOR. 2015. URL: https://jochen-hoenicke.de/trezor-power-analysis/.
M. Arapinis, A. Gkaniatsou, and A. Kiayias, “Low-Level Attacks in Bitcoin Wallets“ International Conf. on Info. Security (ISC), 2017.
Wouter de Boer, “Power Analysis of the Ledger Nano S” Bachelor thesis, Computer Science, Radboud University, 2018.
Ledger Donjon https://www.sstic.org/2019/presentation/side_channel_assessment_hardware_wallets/

## Slide 32: Screaming channels: When electromagnetic side channels meet radio transceivers. (ACM, CCS, 2018)
Digital + Analog/RF Circuits (Mixed-Signal): on the same silicon die.
Digital Noise → Substrate Coupling → Radio Transmission
G. Camurati, S. Poeplau, M. Muench, T. Hayes, and A. Francillon. Screaming channels: When electromagnetic side channel smeet radio transceivers. ACM Conferenceon Computer and Communications Security, CCS, 2018.
nRF51822 Bluetooth LE 2.4GHz

## Slide 33: Screaming channels: From a Detailed Analysis to Improved Attacks (IACR, TCHES, vol. 2020-3) Far Field EM Side-Channel Attack on AES Using Deep Learning (ACM, ASHES, 2020)
G. Camurati, A. Francillon, F.-X. Standaert, "Understanding Screaming Channels: From a Detailed Analysis to Improved Attacks." IACR TCHES 2020 vol. 3
R. Wang, H. Wang, and E. Dubrova, "Far Field EM Side-Channel Attack on AES Using Deep Learning" ACM Workshop on Attacks and Solutions in Hardware Security (ASHES), 2020.

## Slide 34: A Side Journey to Titan Side Channel Attack on Google Titan Security Key (2021)
Secret Key of the Google Titan Security Key (US version) can be cloned by attackers (under some attack scenario)
Runs the FIDO U2F (Universal Second Factor) Protocol
https://ninjalab.io/a-side-journey-to-titan/
https://store.google.com/ca/product/titan_security_key?hl=en-GB
Notes: 這篇論文是 2021 年法國 Ninja 實驗室發表的成果，是 Usenix Security 的論文。
結論就是 Google Titan 這顆晶片的 Security Key 可以被攻擊者完全攻擊出來。
由於 Google Titan Security chip 是來自於 NXP 的某個類型晶片，所以其實 NXP 的很多系列晶片，也一併受到影響。

## Slide 35
https://ninjalab.io/a-side-journey-to-titan/
Notes: 因為 Google 當然不會告訴你用什麼晶片，所以找一個類似的晶片，例如 NXP A700x 這顆的 Family，在這篇論文取名 Rhea (土星的第二大衛星)， 在架設 Rhea 這顆晶片的環境後，我們可以在上面執行數位簽章等運算。
然後再它運行的時候去做旁通道量測，再藉由量測結果去比對 Google Titan 的結果，這樣才可以知道量測到裡洩漏了什麼資訊。 Rhea 是跑 JavaCard 的作業系統，所以在這上面可以看到的是 JavaCard (在 applet, 上執行 ECDSA 簽章)

## Slide 36: A Side Journey to Titan Side Channel Attack on Google Titan Security Key (2021)
Other possibly impacted products
  Several NXP JavaCard smartcards based on P5x chips
  Google Titan Security Key (EU version)
  Yubico Yubikey Neo
  Feitian FIDO NFC USB-A / K9, MultiPass FIDO / K13,
  Feitian ePass FIDO USB-C/ K21, FIDO NFC USB-C/ K40
https://ninjalab.io/a-side-journey-to-titan/
https://store.google.com/ca/product/titan_security_key?hl=en-GB

## Slide 37: CVE, Common Vulnerabilities and Exposures

## Slide 38: CVE, Common Vulnerabilities and Exposures

## Slide 39: 5. Advanced Encryption Standard
https://link.springer.com/book/10.1007/978-3-642-04101-3
https://www.mpi-sp.org/39026/christof-paar
https://www.hshl.de/personen/prof-dr-ing-jan-pelzl
Max Planck Institute for Security and Privacy
Jan Pelzl
Christof Paar
University of Applied Sciences, Hamm-Lippstadt
Understanding cryptography (Ch.4)

## Slide 40: AES
Overview of the AES algorithm
Internal structure of AES
  Byte Substitution layer
  Diffusion layer
  Key Addition layer
  Key schedule
Decryption
Practical issues

## Slide 41: Overview of the AES algorithm
AES is the most widely used symmetric cipher today
The algorithm for AES was chosen by the US National Institute of Standards and Technology (NIST) in a multi-year selection process
The requirements for all AES candidate submissions were:
  Block cipher with 128-bit block size
  Three supported key lengths: 128, 192, and 256 bits
  Security relative to other submitted algorithms
  Efficiency in software and hardware

## Slide 42: Chronology of the AES Selection
The need for a new block cipher was announced by NIST in January 1997
15 candidates algorithms were accepted in August 1998 and 5 finalists were announced in August 1999:
  Rijndael – J. Daemen & V. Rijmen
  Serpent – Eli Biham et al.
  Twofish – B. Schneier et al.
  RC6 – RSA Laboratories
  Mars – IBM Corporation
In October 2000, Rijndael was chosen as the AES. And AES was formally approved as a US federal standard in November 2001

## Slide 43: AES: Overview
The number of rounds depends on the chosen key length:
Key length (bits) | Number of rounds
128 | 10
192 | 12
256 | 14

## Slide 44: AES: Overview
Iterated cipher with 10/12/14 rounds
Each round consists of “Layers”

## Slide 45: AES: Overview
https://www.youtube.com/watch?v=mlzxpkdXP58

## Slide 46: Internal structure of AES
AES is a byte-oriented cipher
The state A (i.e., the 128-bit data path) can be arranged in a 4  4 matrix:
with A0, …, A15 denoting the 16-byte input of AES
A0 | A4 | A8 | A12
A1 | A5 | A9 | A13
A2 | A6 | A10 | A14
A3 | A7 | A11 | A15

## Slide 47: Internal Structure of AES
Round function for rounds 1, 2, …, nr –1:
Note: In the last round, the MixColumn tansformation is omitted

## Slide 48: Byte Substitution Layer
This layer consists of 16 S-Boxes with the following properties:
  Identical, The only nonlinear operation of AES,
  i.e., ByteSub(Ai) + ByteSub(Aj) ≠ ByteSub(Ai + Aj), for i, j = 0, …, 15
  Bijective, i.e., there exists a one-to-one mapping of input and output bytes  S-Box can be uniquely reversed
In software implementations, the S-Box is usually realized as a lookup table

## Slide 49
The Diffusion layer
provides diffusion over all input state bits
consists of two sublayers:
  ShiftRows Sublayer: Permutation of the data on a byte level
  MixColumn Sublayer: Matrix operation which combines (“mixes”) blocks of four bytes
performs a linear operation on state matrices A, B, i.e.,
DIFF(A) + DIFF(B) = DIFF(A + B)
Diffusion Layer

## Slide 50: ShiftRows Sublayer
Rows of the state matrix are shifted cyclically:
Input matrix:
Output matrix:
B0 | B4 | B8 | B12
B1 | B5 | B9 | B13
B2 | B6 | B10 | B14
B3 | B7 | B11 | B15
B0 | B4 | B8 | B12
B5 | B9 | B13 | B1
B10 | B14 | B2 | B6
B15 | B3 | B7 | B11
no shift
← one position left shift
← two positions left shift
← three positions left shift

## Slide 51: MixColumn Sublayer
Linear transformation which mixes each column of the state matrix
Each 4-byte column is considered as a vector and multiplied by a fixed 4  4 matrix, e.g.,
where 01, 02 and 03 are given in hexadecimal notation
All arithmetic is done in the Galois field GF(28)

## Slide 52: Key Addition Layer
Inputs:
  16-byte state matrix C
  16-byte subkey ki
Output: C  ki
The subkeys are generated in the key schedule

## Slide 53: Key Schedule
Subkeys are derived recursively from the original 128/192/256-bit input key
Each round has 1 subkey, plus 1 subkey at the beginning of AES
Key whitening: Subkey is used both at the input and output of AES  # subkeys = # rounds + 1
There are different key schedules for the different key sizes
Key length (bits) | Number of subkeys
128 | 11
192 | 13
256 | 15

## Slide 54: Key Schedule
Example: Key schedule for 128-bit key AES
Word-oriented: 1 word = 32 bits
11 subkeys are stored in W [0], … , W [3], W [4], … , W [7], … , W [40], … , W [43]
First subkey W [0]…W [3] is the original AES key

## Slide 55: Key Schedule
Function g rotates its four input bytes and performs a bytewise S-Box substitution  nonlinearity
The round coefficient RC is only added to the leftmost byte and varies from round to round: RC[1] = x0 = (00000001)2
RC[2] = x1 = (00000010)2
RC[3] = x2 = (00000100)2 ...
RC[10] = x9 = (00110110)2
x i represents an element in a Galois field

## Slide 56: Decryption
AES is not based on a Feistel network  All layers must be inverted for decryption:
  MixColumn layer →
  Inv MixColumn layer
  ShiftRows layer →
  Inv ShiftRows layer
  Byte Substitution layer →
  Inv Byte Substitution layer
  Key Addition layer is its own inverse

## Slide 57: Decryption
Inv MixColumn layer:
  To reverse the MixColumn operation, each column of the state matrix C must be multiplied with the inverse of the 4  4 matrix, e.g.,
  where 09, 0B, 0D and 0E are given in hexadecimal notation
Again, all arithmetic is done in the Galois field GF(28)

## Slide 58: Decryption
Inv ShiftRows layer:
  All rows of the state matrix B are shifted to the opposite direction:
  Input matrix:
  Output matrix:
B0 | B4 | B8 | B12
B1 | B5 | B9 | B13
B2 | B6 | B10 | B14
B3 | B7 | B11 | B15
B0 | B4 | B8 | B12
B13 | B1 | B5 | B9
B10 | B14 | B2 | B6
B7 | B11 | B15 | B3
no shift
→ one position right shift
→ two positions right shift
→ three positions right shift

## Slide 59: Decryption
Inv Byte Substitution layer:
  Since the S-Box is bijective, it is possible to construct an inverse, such that Ai = S –1(Bi) = S –1(S(Ai))
   The inverse S-Box is used for decryption. It is usually realized as a lookup table.
Decryption key schedule:
  Subkeys are needed in reversed order (compared to encryption)
  In practice, the same key schedule is used for encryption and decryption. This requires that all subkeys must be computed before the encryption of the first block can begin

## Slide 60: Implementation in Software
One requirement of AES was the possibility of an efficient software implementation
Straightforward implementation is well suited for 8-bit processors (e.g., smart cards), but inefficient on 32-bit or 64-bit processors

## Slide 61: Implementation in Software
A more sophisticated approach: Merge all round functions (except the key addition) into one table look-up
  This results in four tables with 256 entries, where each entry is 32 bits wide
  One round can be computed with 16 table look-ups
Typical SW speeds are more than 1.6 Gbit/s on modern 64-bit processors

## Slide 62: Security
Brute-force attack: Due to the key length of 128, 192 or 256 bits, a brute-force attack is not possible
Analytical attacks: There is no analytical attack known that is better than brute-force
Side-channel attacks:
  Several side-channel attacks have been published
  Note that side-channel attacks do not attack the underlying algorithm but the implementation of it

## Slide 63: Lessons Learned
AES is a modern block cipher that supports three key lengths of 128, 192, and 256 bits. It provides excellent long-term security against brute-force attacks.
AES has been studied intensively since the late 1990s, and no attacks have been found that are better than brute-force.
AES’s basic operations use Galois field arithmetic and provide strong diffusion and confusion.

## Slide 64: Lessons Learned
AES is part of numerous open standards, such as IPsec or TLS, and is the mandatory encryption algorithm for US government applications.
It seems likely that the cipher will be the dominant encryption algorithm for many years.
AES is efficient in software and hardware.

## Slide 65: 6. Power Analysis
Side-Channel Analyses (Attacks)
  SPA (Simple Power Analysis)
  DPA (Differential Power Analysis)
    DoM (Difference of Means)
    CPA (Correlation Power Analysis)
    MIA (Mutual Information Analysis)
    LR-Based Attacks (Linear Regression)
    ….

## Slide 66: Simple Power Analysis
Elliptic Curve Cryptography (ECC)
    Scalar multiplication: compute
    : a private key, Example: Double-and-add method
Simple Power Analysis:
https://en.wikipedia.org/wiki/Elliptic_curve_point_multiplication
Notes: 橢圓曲線密碼學，基於離散對數問題，Q=dP, 知道 P, Ｑ很難求 d；一般選擇完適合的曲線後，Base point P 也同時決定。
基於 P 再生成公鑰 Q 的時候，最簡單的方式，是 Double-and-add method。
也就是將私鑰 d 用二進位展開，遇到 0 的時候，做一個 Double, 遇到 1 的時候呢，做一個 Double 再做一個 Add.
運算的過程中，如果 Double 與 Add 的功率消耗曲線不同，如圖所示，就很有可能被解出私鑰的數值。
例如 Double-and-add method 運算時，將中間的功率消耗記錄下來，變成這樣的曲線。
然後我門找尋裡面的波形特徵， Double 長什麼樣，Add 長什麼樣，然後整個列出來之後，寫出對應的數字，一個 double, 一個 add 對應到一個 1, 單純只有一個 double 對應到一個 0；因此展開成二進制 之後，我們知道是 d = 75。
橢圓曲線密碼學，基於離散對數問題，Q=dP, 知道 P, Ｑ很難求 d；因此一般選擇完適合的曲線後，Base point P 也同時決定。
基於 P 再生成公鑰 Q 的時候，最簡單的方式，是 Double-and-add method。也就是將私鑰 d 用二進位展開，遇到 0 的時候，做一個 Double, 遇到 1 的時候呢，做一個 Double 再做一個 Add.
因此，假設我們要生成 Q=75P 這個公鑰，所以將 75 展開成二進制 (1001011)_2 ，做 Double and Add 運算。
運算的過程中，如果 Double 與 Add 的功率消耗曲線不同，如圖所示，就很有可能被解出私鑰的數值。

## Slide 67
Advised: Feb. 2015 – Oct. 2018
https://www.cl.cam.ac.uk/~sps32/

## Slide 68: How DPA Works?
Fortunately, the 16 bytes are independent of each other before MixColumn in the first rounds.
MixColumn
SubByte
Fisrt round key
Divid and Conquer!
X128 to 16x 28

## Slide 69: Some Popular Models
Bit model
  Only take one bit into consideration
  Example: the LSB of the intermediate value
Hamming distance model
  HD (previous state present state)
Hamming weight model
  HW (state)
Zero-Value Model
  The data value 0 is lower than the power consumption for all other values.

## Slide 70: Power Analysis Models
Take hypothetical intermediate values as input, and output hypothetical power consumptions.
Power model: Power = a ‧ # bitflips + n
  a : power consumption from components
  n : normal distribution noise
Hamming Weight: HW (10100100) = 3
Hamming Distance: HD (00110101, 00100111) = 2
S. Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards. New York, NY, USA: Springer, 2006, Ch. 3.
François-Xavier Standaert, Introduction to Side-Channel Attacks, Secure Integrated Circuits and Systems, NY, USA: Springer , 2010, pp. 27-42.

## Slide 71: Differential Power Analysis
Compared to SPA, DPA
  Do not need detailed knowledge about the devices
  Usually need a large amount of traces that operate on different data
  Need to process the devices
Three disciplines
  Cryptanalysis: Target a good intermediate value
  Engineering: Get Side-Channel leakage precisely
  Statistics: Verify key hypothesis

## Slide 72: Differential Power Analysis
S. Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards. New York, NY, USA: Springer, 2006

## Slide 73: Differential Power Analysis
S. Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards. New York, NY, USA: Springer, 2006

## Slide 74: Choosing an Intermediate Value
A good intermediate value
  Depends on part of key and plaintext /ciphertext: f(p,k) or f(c,k’)
  A non-linear f is better: such as the output of Sbox
  Examples:
    Sbox (p⊕k)
    Sbox-1(ShiftRow(c⊕k’))
Calculate hypothetical intermediate values for every possible key candidates

## Slide 75: Correlation Coefficients
Assumption: the linearity between power consumption and #bitflips
Pearson’s correlation coefficient detects the linear dependencies of two variables

## Slide 76: Correlation Power Analysis, CPA
Use correlation coefficient as statistical test
Proposed at 2004
  Eric Brier, Christophe Clavier, Francis Olivier. Correlation Power Analysis with a Leakage Model. CHES 2004: pp.16-29
  2023/10/12 Times Cited: 3127
One of the most popular DPA attacks, usually used as a baseline DPA

## Slide 77: CPA Workflow
Choosing an intermediate value
Measuring the power consumptions
Calculating hypothetical intermediate values
Mapping intermediate values to hypothetical power consumption (Power model)
Comparing the hypothetical consumption with real power consumption (Statistics test)

## Slide 78: Analytics Workflow
Step 1: Choose the target intermediate value
Example: on AES-128
The 16 bytes are independent before MixColumns in the first round
So we can process it byte by byte
Divide and Conquer!!
https://en.wikipedia.org/wiki/Advanced_Encryption_Standard
Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards. New York, NY, USA: Springer, 2006
Step 2: Measure the power traces
1 (D=1) x T (points)
Targeted intermediate value

## Slide 79: Analytics Workflow
0x3128A6DA……7C
0xA24B6E1D……97
0x6C7B32C…...…82
…
Plaintexts
-0.388
0.021
0.734
-0.172
0.053
0.681
0.073
-0.105
0.592
…
…
…
…
Traces
D records
D recodes and Sampling T
D x 16(Byte)
D x T(points)
Step 2: Measure the power traces (record data)
S. Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards. New York, NY, USA: Springer, 2006
1 (D=1) x T (points)
Notes: 在明文：D 筆記錄，每條記錄丟 128 bits (16Byte) 進去，對應到 D 比記錄，每筆記錄有 T 個量測點

## Slide 80: Analytics Workflow
0x31
0xA2
0x6C
0x00
0x01
0xFF
Calculate hypothetical intermediate value
Sbox (p ⊕ k)
0xC7
0x37
0x50
0x04
0x0A
0x8B
0x4C
0xDC
…
…
…
…
…
…
0x3C
Plaintexts (first byte)
Key hypothesis (256 kinds)
D x 1(Byte)
1 x K, (K=256)
D x 256
Power model
HW(‧)
Step 3: Choose a power model
S. Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards. New York, NY, USA: Springer, 2006
Notes: 將每 D 筆記錄 的第一個 Byte, 分別與一個 Byte 的 256 種可能，經過 S-Box 的中間值運算，得到一個 D x 256 的大矩陣。 挑選適合的 Model。以這個例子來說， D x 256 這個大矩陣的左下角，是16 進位的 0x50。

## Slide 81: Analytics Workflow
5
5
2
1
2
4
3
5
Statistical model
correlation(‧ , ‧)
-0.388
0.021
0.734
-0.172
0.053
0.681
0.073
-0.105
0.592
…
…
…
…
…
…
…
…
4
Traces
D x K
D x T
Step 4: Calculate the hypothetical intermediate value and corresponding hypothetical power consumption
0x50 =10010000
Notes: D x 256 大矩陣左下角是16 進位的 0x50，對應到適合的 Model 數值是 2 ，再與之前量到的 D X T 的大矩陣經過 Correlation 的運算

## Slide 82: Analytics Workflow
Step 5: Apply the statistic analysis between measured power consumption and hypothetical power consumption
0.181
0.005
-0.124
-0.103
0.013
0.090
-0.001
-0.131
0.095
…
…
…
…
Correlation coefficients matrix
Key 0x00
Key 0x01
Key 0xFF
0x13 is the correct key of the first byte !
-0.084
0.053
0.372
Key 0x13
…
…
K x T
…
…
Notes: 得到一個 K x T 的矩陣。這時候我們可以看，相關性最高的是我們猜 0x00-0xFF 哪個數值，就猜這 AES 128 Key 的第一個 Byte 數值為這個。 舉例來說，這個例子是 0x13 這個結果。

## Slide 83: Measurement Results

## Slide 84: Remarks
Why is the Hamming Weight model suitable?
  In software case, the intermediate value may be moved between register and memory several times
  Bus may be precharged before moving data
For hardware circuits, Hamming Distance model may be more suitable.

## Slide 85: Choosing an Statistics Test
Fact: the linearity between power consumption and #bitflips (i.e. Hamming distance)
So Pearson’s correlation coefficient is a well-suited statistics test since it detects the linear dependencies of two variables
That is so-called “Correlation Power Analysis (CPA)”

## Slide 86: Results by Hamming weight model

## Slide 87: Countermeasures
Hiding : Breaking the link between the power consumption of the devices and the processed data values.
Dual-rail, Pre-charge logic cell:
  Parallel computing:
  Shuffling:
S. Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards., NY, USA: Springer, 2006
DRP cell
a
a’
b
b’
a+b
(a+b)’
S1
S2
S3
S15
…
S16
S11
S3
S7
S6
S1
S1
S2
S16
…

## Slide 88: Countermeasures
  Masking:
  Without changing the power consumption of the device.
  Each intermediate value v is concealed by a random value m that is called mask: vm = v * m.
Q’
function
mask process
⊕
P
m
Q
m’
⊕
Q
(P ⊕ m)
S. Mangard, E. Oswald, and T. Popp, Power Analysis Attacks: Revealing the Secrets of Smart Cards., NY, USA: Springer, 2006
Notes: 不改變原本 Device 原本的特性，而達到防護的效果。

## Slide 89: Conclusion
Cryptography
Hardware
Software
Side Channel Analysis
Cache Attacks; Signal processing
Invasive Attack
Embedded System

## Slide 90
Paul Kocher, Joint invited talk with CRYPTO, CHES 2016 http://www.chesworkshop.org/ches2016/presentations/CHES16_invited.pdf

## Slide 91
Paul Kocher, Joint invited talk with CRYPTO, CHES 2016 http://www.chesworkshop.org/ches2016/presentations/CHES16_invited.pdf
Paul Kocher, Joint invited talk with CRYPTO, CHES 2016 http://www.chesworkshop.org/ches2016/presentations/CHES16_invited.pdf

## Slide 92
How to Start…..
Kung Fu Hustle, https://en.wikipedia.org/wiki/Kung_Fu_Hustle

## Slide 93: Conclusion
Right-Hand Circular Polarization, RHCP
Verification or Penetration test
Attack or Analysis
Defense or Countermeasure